## Slide 1
Mohamed Abuella¹, Adib Allahham¹, Sara Louise Walker²
¹ Northumbria University, UK ² University of Birmingham, UK
9th International Conference on Environment Friendly Energies and Applications
EFEA 2025, Newcastle upon Tyne, UK. 4-5 December 2025
Paper ID:40
Socio‑Technical, Electrification, and Hydrogen‑Driven Pathways for Residential Heating Decarbonisation in the North of Tyne

## Slide 2: Motivation
Decarbonisation Pathways for Residential Heating, North of Tyne – EFEA 2025
Motivation and Objectives
• Assess socio‑technical interventions
• Evaluate heat pump and hydrogen boiler uptake
• Analyse hydrogen blending impacts
• Identify investment and system efficiency pathways
It is same technology but depending on where you live. … So, we cannot follow a single blueprint!

## Slide 3: Overview
North of Tyne (NoT)
• 85% of UK homes use natural gas
• NoT consumed 17.3 TWh gas (2018)
• High fuel poverty and ageing housing
• Need for coordinated, low‑carbon strategies
Decarbonisation Pathways for Residential Heating, North of Tyne – EFEA 2025
Daily Profile of Total Electricity Demand for NoT in 2019
Demand Overview
We use the coldest day in November 2019 as a baseline to model peak demand.
This day saw total consumption of 31 GWh, with gas (24 GWh) significantly outpacing electricity (7 GWh).
Daily Profile of Total Gas Demand for NoT in 2019
North of Tyne (NoT)

## Slide 4
Bi-level optimisation framework:
Upper layer for long-term planning,
Lower layer for short-term operation.
Methodology
Decarbonisation Pathways for Residential Heating, North of Tyne – EFEA 2025
Integrated multi-vector energy system framework for NoT region
-NI
GTM framework for integrated energy system planning
Integrated multi‑vector system: Electricity, gas, and hydrogen.
where:
Coupling units provide system flexibility via multi-vector conversion and storage.

## Slide 5
Decarbonisation Pathways for Residential Heating, North of Tyne – EFEA 2025
From the literature, we evaluate how social-based interventions impact electricity and gas demand profiles in North of Tyne (NoT) region.
Scenario | Intervention | Effect on Gas Demand | Effect on Electricity Demand
1 | Decreasing the heating set point by 2°C | 20% decrease | No effect
2 | Improving the whole building insulation level similar to Passivhaus standards | 77% decrease | No effect
3 | Delay start of heating from October to November | 5.5% decrease | No effect
4 | Use of radiator valves to turn off heating in unoccupied rooms | 4% decrease | No effect
5 | Use of heat pumps | 10% decrease | 14% increase
6 | Use of hydrogen boilers | 10% decrease | No effect
Formulation of Social and Technical Interventions (STIs) of Residential Heating in NoT
Social and Technical Interventions (STI)
Methodology

## Slide 6
Gas Demand
Electricity Demand
Decarbonisation Pathways for Residential Heating, North of Tyne – EFEA 2025
Let G0 and E0 represent the baseline gas and electricity demands, respectively. The adjusted demands G and E after applying a random intervention Ij .
The Monte Carlo simulation of heating interventions indicates a noticeable reduction in gas demand, with only a marginal increase in electricity demand.
Monte Carlo Simulation for Social and Technical Interventions of Heating Demand
Monte Carlo Simulation
Methodology
We applied Monte Carlo simulation for the social and technical Interventions (STI) to simulate their impacts on demand profiles.

## Slide 7
Hydrogen Blending:
(1) No hydrogen; natural-gas baseline – (0%)
(2) Partial blend; low-disruption transition – (20%)
(3) Full hydrogen conversion; major network change – (100%)
Heating Technologies:
(a) Socio-technological interventions – (STI)
(b) 50% heat pumps (HP) and 50% hydrogen (HB) – (50/50 HP–HB)
(c) 100% heat pumps – (100% HP)
(d) 100% hydrogen boilers – (100% HB)
Decarbonisation Pathways for Residential Heating, North of Tyne – EFEA 2025
Case Study
Electricity Network
(Aggregated)
Gas / Hydrogen Network (Aggregated)

## Slide 8
Decarbonisation Pathways for Residential Heating, North of Tyne – EFEA 2025
Results
Hydrogen Blending | 0% H₂ |  |  | 20% H₂ |  |  | 100% H₂ |  | 
Scenario / Metric | Opex | Emis | NPV | Opex | Emis | NPV | Opex | Emis | NPV
STI | 0.64 | 0 | 486 | 0.67 | 0 | 384 | 2.03 | 0 | 323
50/50 HB & HP | 0.82 | 9 | 518 | 0.83 | 8 | 411 | 1.10 | 0 | 253
100% HP | 0.60 | 0 | 419 | 0.65 | 0 | 316 | 1.95 | 0 | 323
100% HB | 1.16 | 0 | 624 | 1.19 | 0 | 519 | 1.93 | 0 | 318
Operational cost (Opex, million £/day), emissions, (tonnes CO2/day), and net present value (NPV, million £) for peak demand in 2050 (full CCS deployment). CCS=Carbon Capture and Storage.
Heat Pump with COP=3
Prices: Electricity=125£/MWh, Natural gas= 37£/MWh, Hydrogen = 75£/MWh
STI: Socio-Technological Interventions
HP: Heat Pumps
HB: Hydrogen Boilers

## Slide 9
Decarbonisation Pathways for Residential Heating, North of Tyne – EFEA 2025
(a) Socio-technological interventions (STI)
(b) 50% heat pumps and 50% hydrogen
(c) 100% heat pumps (100% HP)
(d) 100% hydrogen boilers (100% HB)
Investment planning (100% hydrogen blending, CCS from 2040)
Results

## Slide 10
Decarbonisation Pathways for Residential Heating, North of Tyne – EFEA 2025
Conclusions
Heat pumps: lowest-cost decarbonisation.
Hydrogen: flexible backup, higher running costs.
Demand-side measures help affordability but are insufficient alone.
CCS needed for (near) net-zero with any blue H2 or gas backup.
Best pathway: demand cuts + electrification + targeted H2 + CCS.
Success depends on integrated planning and public engagement.

## Slide 11
Thank You for Your Attention
Any Questions?
Socio‑Technical, Electrification, and Hydrogen‑Driven Pathways for Residential Heating Decarbonisation in the North of Tyne
mohamed.abuella@northumbria.ac.uk
9th International Conference on Environment Friendly Energies and Applications
EFEA 2025, Newcastle upon Tyne, UK. 4-5 December 2025